## Slide 1: Modelling Smart FPGA Switches in the Network
Benji Levine
Supervised by Suhaib Fahmy

## Slide 2: What are FPGAs?
Field-Programmable Gate Array
Flexible Logic ---------------------------------
Flexible routing -------------------------------
Flexible IO ------------------------------------
Embedded hard modules --------------------
LUTs
Large grid of wires and switch boxes
Support for 10G Ethernet, SATA, PCIe
Block memory, DSP blocks
Notes: Flexible logic: basic configurable block to implement combinational logic, coupled with clocked elements to enable synchronous logic and pipelining
Flexible routing: significant chip area dedicated to wires and switch boxes that enable connections between all components
Flexible IO: multi-standard interfacing to external pins, with a range of speed capabilities
Embedded hard modules: an increasing number of different resources optimised for speed and area, including DSP functions and memories

## Slide 3: What are FPGAs?
Field-Programmable Gate Array
Flexible Logic
Flexible routing
Flexible IO
Embedded hard modules
Notes: Flexible logic: basic configurable block to implement combinational logic, coupled with clocked elements to enable synchronous logic and pipelining
Flexible routing: significant chip area dedicated to wires and switch boxes that enable connections between all components
Flexible IO: multi-standard interfacing to external pins, with a range of speed capabilities
Embedded hard modules: an increasing number of different resources optimised for speed and area, including DSP functions and memories

## Slide 4: Networking Concepts
OSI Network Model
TCP / IP network stack
Application
Presentation
Session
Transport
Network
Link
Internet
Physical
Data Link

## Slide 5: Networking Concepts
OSI Network Model
TCP / IP network stack
Application
Transport
Internet
Link
Software Defined Networking
Control plane
Data plane
P4
OpenFlow (part of Mininet)
Notes: SDN separates the control plane from the data plane
Gives the programmer more direct and clear control over how routing decisions are made.
Separates the network control, known as the control plane, from the forwarding process, known as the data plane.
The control plane makes decisions about packets which are either destined to or originally from the current host, while the data plane makes decisions about packets which are going through the host.
The control plane also maintains the routing table, which is used by both planes to make routing decisions
P4 is a language for programming data plane. Sep 2014.

## Slide 6: Why Smart FPGA Switches?
Cloud computing
High latencies
Large data centres
Amazon Web Services (AWS)
Microsoft Azure
Google Cloud Platform
Apache Hadoop

## Slide 7: Why Smart FPGA Switches?
Cloud computing
Existing solutions
“Edge” / “gateway” nodes
Mainframes
NetFPGA
Software Defined Networking (SDN)

## Slide 8: Why Smart FPGA Switches?
Cloud computing
Existing solutions
Drawbacks
Similar to data centres
Latency
Security
Scalability

## Slide 9: Why Smart FPGA Switches?
Cloud computing
Existing solutions
Drawbacks
Solution
Do not divert data from existing path
Appropriate device for computation
Fast
Slow
Static
Flexible
ASIC
FPGA
CPU

## Slide 10: Why Smart FPGA Switches?
Cloud computing
Existing solutions
Drawbacks
Solution
FPGAs
Custom compute architectures – very low latency
Partial reconfiguration
Specific hardware for each algorithm

## Slide 11: Why Smart FPGA Switches?
Cloud computing
Existing solutions
Drawbacks
Solution
FPGAs
Partial reconfiguration
Specific hardware for each algorithm

## Slide 12: Mininet
Virtual network application
Python API
Open Source
Broad tool
Scalable
Dependency chain
Bash script for installation

## Slide 13: NetFPGA
PCI Express interface
Xilinx Virtex / Kintex
4 x 1Gbps – 10Gbps Ethernet
Open source software
1G, 10G, SUME, CML

## Slide 14: Project Management
Kanban Board (Trello)
Weekly meetings
git
Agile
Licensing issues
Access to tools

## Slide 15: Software Development
Python
Open Source (GitHub)
Git submodule
Atom, pycharm
Pylint
Click. Logging, numpy

## Slide 16: Model Results
Get a graph

## Slide 17: Applications
Internet of Things (IoT)
Education
Military
Education

## Slide 18: Demo